## Slide 1: Smashing the Gadgets: Hindering Return-Oriented Programming Using In-Place Code Randomization
Vasilis Pappas, Michalis Polychronakis, and Angelos D. Keromytis
Columbia University

## Slide 2: Machine Code-Level Attacks & Defenses
Code Injection
W⊗X
Code-reuse
ASLR

## Slide 3: Information Leaks Break ASLR [Ser12]

## Slide 4: ASLR is Not Fully Adopted
Executable programs in Ubuntu Linux
  Only 66 out of 1,298 binaries in /usr/bin [SAB11]
Popular third-party Windows applications
  Only 2 out of 16 [Pop10]

## Slide 5: This Work
Code randomization
Applicable on third-party applications
(Practically) Zero performance overhead

## Slide 6: Overview
Background
In-place code randomization
Results
Summary

## Slide 7: Return-Oriented Programming
0xb8800000
0x00000001
0xb8800010
0x00000002
0xb8800020
0xb8800010
0x00400000
0xb8800030
Stack
Code
0xb8800000:
pop eax
ret
...
0xb8800010:
pop ebx
ret
...
0xb8800020:
add eax, ebx
ret
...
0xb8800030:
mov [ebx], eax
ret
esp
Actions
eax = 1
ebx = 2
eax += ebx
ebx = 0x400000
*ebx = eax
Notes: Define gadgets. Attackers can use them, may correspond to intended or unintended instruction sequences.

## Slide 8: ROP Defenses
Performance Overhead
Low High
Program binary Source code
Requires
ROPdefender
[DSW11]
DROP
[CXS+09]
DROP++
[CXH+11]
G-Free
[OBL+10]
Return-less
[LWJ+10]
CFL
[BJF11]

## Slide 9: Why In-Place?
Randomization usually changes the code size
  Need to update the control-flow graph (CFG)
But, accurate static disassembly of stripped binaries is hard
  Incomplete CFG (data vs. code)
  Code resize not an option
Must randomize in-place!
Notes: I’ll show simple examples to make it easier to understand and less boring.

## Slide 10: Randomizations
Instruction Substitution
Instruction Reordering
  Intra Basic Block
  Register Preservation Code
Register Reassignment

## Slide 11: Instruction Substitution
mov al,0x1
cmp al,bl
lea eax,[ebp-0x80]
add [edx],edi
ret
mov al,0x1
cmp bl,al
lea eax,[ebp-0x80]
add [eax],edi
fmul [ebp+0x68508045]
B0 | 01 | 3A | C3 | 8D | 45 | 80 | 50 | 68
B0 | 01 | 38 | D8 | 8D | 45 | 80 | 50 | 68
Notes: Mention that this is part of the original code!

## Slide 12: Instruction Reordering (Intra BBL)
8B 41 10 mov eax,[ecx+0x10]
53 push ebx
8B 59 0C mov ebx,[ecx+0xC]
3B C3 cmp eax,ebx
89 41 08 mov [ecx+0x8],eax
7E 4E jle 0x5c
59 push ebx
0C 3B or al,0x3B
C3 ret

## Slide 13: Instruction Reordering (Intra BBL)
8B 41 10 mov eax,[ecx+0x10]
53 push ebx
8B 59 0C mov ebx,[ecx+0xC]
3B C3 cmp eax,ebx
89 41 08 mov [ecx+0x8],eax
7E 4E jle 0x5c
41 inc ecx
10 89 41 08 3B C3
adc [ecx-0x3CC4F7BF],cl

## Slide 14: Register Preservation Code Reordering
push ebx
push esi
mov ebx,ecx
push edi
mov esi,edx
.
.
.
pop edi
pop esi
pop ebx
ret
push edi
push ebx
push esi
mov ebx,ecx
mov esi,edx
.
.
.
pop esi
pop ebx
pop edi
ret
Prolog
Epilog

## Slide 15: Register Reassignment
eax
edi
Live regions
function:
push esi
push edi
mov edi,[ebp+0x8]
mov eax,[edi+0x14]
test eax,eax
jz 0x4A80640B
mov ebx,[ebp+0x10]
push ebx
lea ecx,[ebp-0x4]
push ecx
push edi
call eax
...
function:
push esi
push edi
mov eax,[ebp+0x8]
mov edi,[edi+0x14]
test edi,edi
jz 0x4A80640B
mov ebx,[ebp+0x10]
push ebx
lea ecx,[ebp-0x4]
push ecx
push eax
call edi
...

## Slide 16: Implementation – Orp
Focused on the Windows platform
  Could be integrated in Microsoft’s EMET
CFG is extracted using IDA Pro
  Implicitly used registers
  Liveness analysis (intra and inter-function)
  Register categorization (arg., preserved, etc.)
  Randomizations
  Binary rewriting (relocations fixing, etc.)

## Slide 17: Evaluation
Correctness and performance
  Execute Wine’s test suite using randomized versions of Windows DLLs
Randomization Coverage
Real-World Exploits
ROP Compilers
Notes: After explaining wine test, mention that this is where we also measured performance

## Slide 18: Randomization Coverage
Chart: Modifiable Gadgets (%)
| Instruction Substitution | Intra Basic Block Reordering | Register Preservation Code Reordering | Register Reassignment | Total
Series 1 | 17 | 37 | 53 | 46 | 0
series 2 | 0 | 0 | 0 | 0 | 82
Dataset: 5,235 PE files (~0.5GB code) from Windows, Firefox, iTunes and Reader

## Slide 19: Real-World Exploits
Exploit/Reusable Payload | Unique Gadgets | Modifiable | Combinations
Adobe Reader v9.3.4 | 11 | 6 | 287
Integard Pro v2.2.0 | 16 | 10 | 322K
Mplayer Lite r33064 | 18 | 7 | 1.1M
msvcr71.dll (While Phosphorus) | 14 | 9 | 3.3M
msvcr71.dll (Corelan) | 16 | 8 | 1.7M
mscorie.dll (White Phosphorus) | 10 | 4 | 25K
mfc71u.dll (Corelan) | 11 | 6 | 170K
Modifiable gadgets were not always directly replaceable!
Notes: Why aren’t the modifiable gadgets 80%?
Explain the last column!

## Slide 20: ROP Compilers
Mona.py constructs DEP+ASLR bypassing code
  Allocate a WX buffer, copy shellcode and jump
Q [SAB11] is the state-of-the-art ROP compiler
  Designed to be robust against small gadget sets
Is it possible to create a randomization-resistant payload?

## Slide 21: ROP Compilers Results
Non-ASLR Code Base | Mona Orig. Rand. |  | Q Orig. Rand. | 
Adobe Reader v9.3.4 | ✓ | ✗ | ✓ | ✗
Integard Pro v2.2.0 | ✗ | ✗ | ✓ | ✗
Mplayer Lite r33064 | ✓ | ✗ | ✓ | ✗
msvcr71.dll | ✗ | ✗ | ✓ | ✗
mscorie.dll | ✗ | ✗ | ✗ | ✗
mfc71u.dll | ✓ | ✗ | ✓ | ✗
Both failed to construct payloads from non-randomized code!
Notes: Say the story better: if the attackers knew, they would only use non-randomized parts, etc…

## Slide 22: Summary
In-place code randomization
  Requires no source code or debug symbols
  (Practically) Zero performance overhead
  Breaks 80% of gadgets
  Prevented real exploits and ROP compilers
Get the code (Python): http://nsl.cs.columbia.edu/projects/orp
Notes: What about return-to-libc?

## Slide 23: References
[Ser12] Fermin J. Serna. The case of the perfect info leak, 2012.
http://zhodiac.hispahack.com/my-stuff/security/Flash_ASLR_bypass.pdf.
[SAB11] Edward J. Schwartz et al. Q: exploit hardening made easy. USENIX Security, 2011.
[Pop10] Alin Rad Pop. Dep/aslr implementation progress in popular third-party windows applications, 2010.
http: //secunia.com/gfx/pdf/DEP_ASLR_2010_paper.pdf.
[Sha07] Hovav Shacham. The geometry of innocent flesh on the bone: return-into-libc without function calls
(on the x86). CCS, 2007.
[CDD+10] Stephen Checkoway et al. Return-oriented programming without returns. CCS, 2010
[BJFL11] Tyler Bletsch et al. Jump-oriented programming: a new class of code-reuse attack. ASIACCS, 2011.
[LZWG11b] Kangjie Lu et al. Packed, printable, and polymorphic return-oriented programming, RAID, 2011.
[DSW11] Lucas Davi et al. Ropdefender: a detection tool to defend against return-oriented programming
attacks. ASIACCS, 2011
[CXS+09] Ping Chen et al. Drop: Detecting return-oriented programming malicious code, ICISS, 2009.
[CXH+11] Ping Chen et al. Efficient detection of the return-oriented programming malicious code,
ICISS, 2011.
[OBL+10] Kaan Onarlioglu et al. G-free: defeating return-oriented programming through gadget-less
binaries. ACSAC, 2010.
[LWJ+10] Jinku Li et al. Defeating return-oriented rootkits with “return-less” kernels. EuroSys, 2010.
[BJF11] Tyler Bletsch et al. Mitigating code-reuse attacks with control-flow locking. ACSAC, 2011.